## Slide 1
TCS302 - DATA STRUCTURES WITH C
Better Probe Sequences
Quadratic Probing and Double Hashing
Unit III - Lecture 29
Quadratic probing step by i-squared instead of i
Double hashing a second hash function picks the step
Notes: Direct continuation of Lecture 28. Same six keys, same tableSize=7, reused deliberately so every probe count is directly comparable across all three collision-resolution methods.

## Slide 2
LECTURE 29
Recap: linear probing's weakness, and the fix to try
TCS302 - UNIT III
02
Lecture 28: linear probing steps by 1 each time (idx, idx+1, idx+2, ...). This caused SECONDARY CLUSTERING - key 24 needed 3 hops because 9's earlier collision left a solid block of occupied slots in its path.
Today's idea: what if the STEP SIZE itself changed, so probe sequences do not pile up in a straight line?
Quadratic probing: step by 1, then 4, then 9, then 16 (i-squared) - jumps grow quickly, breaking up straight-line pileups.
Double hashing: the STEP SIZE itself comes from a second hash function - two different keys with the same home index usually take completely different paths.
Notes: Frame both techniques as direct responses to the exact clustering problem demonstrated in Lecture 28 - this is not new material appearing from nowhere, it is the fix to a problem already shown.

## Slide 3
LECTURE 29
Quadratic probing: jump by i-squared
TCS302 - UNIT III
03
PART A
idx = (home + i*i) % tableSize, for i = 0, 1, 2, 3, ...
int idx, i = 0;
while (i < TABLE_SIZE)
{
idx = (home + i * i) % TABLE_SIZE;
if (table[idx] == EMPTY)
{
table[idx] = key;
return idx;
}
i++;
}
i=0: check home itself.
i=1: home+1. i=2: home+4. i=3: home+9. The gaps GROW, instead of staying fixed at 1 like linear probing.
Growing gaps mean two colliding keys are unlikely to keep landing on each other's later probes.
Notes: The only code change from Lecture 28's linear probing is the formula for idx - everything else (the while loop, the EMPTY check, the insert/search shape) stays identical. Worth pointing out explicitly how small this change is.

## Slide 4
LECTURE 29
Quadratic probing
TCS302 - UNIT III
04
PART A
0
1
2
3
4
5
6
.
15
23
17
24
12
9
key | home | probe sequence tried | landed at
9 | 2 | i=0:idx2(full), i=1:idx3(full), i=2:idx6(empty) | index 6
24 | 3 | i=0:idx3(full), i=1:idx4(empty) | index 4
Compare with linear probing: 24 needed 3 hops there (landed at index 6). Here it needs only 2 checks and lands at index 4 - quadratic probing genuinely reduced its cost, on this exact key.
Notes: Verified by compiling and running. 9 still needs 3 checks (it collides at both i=0 and i=1 before succeeding at i=2), but 24 improves from 3 hops (linear) to 2 checks (quadratic) - a direct, measured improvement on the identical key and table.

## Slide 5
LECTURE 29
The catch: quadratic probing can fail before the table is full
TCS302 - UNIT III
05
PART A
With tableSize = 8 (NOT prime), the values of i*i % 8 only ever produce {0, 1, 4} - just 3 distinct offsets, no matter how large i grows.
0
1
2
3
4
5
6
7
8
16
.
.
24
.
.
.
insert(32) FAILS here - even though 5 of 8 slots are still empty.
Keys 8, 16, 24, 32 all share home index 0 (each is a multiple of 8).
8, 16, 24 land at indices 0, 1, 4 - exactly the ONLY offsets {0,1,4} reachable from home 0.
32's probe sequence just keeps revisiting 0, 1, 4 forever - it can never reach the 5 genuinely empty slots.
Notes: Verified by running the code exactly as shown: insert(32) prints FAILED. This is why quadratic probing is usually taught alongside the rule 'use a PRIME table size' - with tableSize=7 (prime, as used on the previous slide), this failure mode cannot happen, because i*i % 7 for i=0..6 does cover all 7 residues.

## Slide 6
LECTURE 29
Double hashing: a second hash function picks the step
TCS302 - UNIT III
06
PART B
idx = (home + i * h2(key)) % tableSize, h2(key) = 1 + (key % (tableSize-1))
int h1 = key % TABLE_SIZE;
int step = 1 + (key % (TABLE_SIZE-1));
int idx, i = 0;
while (i < TABLE_SIZE)
{
idx = (h1 + i * step) % TABLE_SIZE;
if (table[idx] == EMPTY)
{
table[idx] = key;
return idx;
}
i++;
}
step depends on the KEY, not just on i - two keys with the same home almost always get different step sizes.
The "+1" in h2 guarantees step is never 0, so the probe sequence always moves.
Choosing tableSize prime again guarantees every slot is eventually reachable.
Notes: h2's '+1' is not decorative - a step of 0 would mean idx never changes, causing an infinite loop on the very first collision. This is a common bug to watch for if students design their own h2.

## Slide 7
LECTURE 29
Double hashing: verified
TCS302 - UNIT III
07
PART B
0
1
2
3
4
5
6
.
15
23
17
24
12
9
key | h1 (home) | h2 (step) | landed at index
9 | 2 | 4 | 6
24 | 3 | 1 | 4
search(9) probe count: linear = 3, quadratic = 3, double hashing = 2.
search(24) probe count: linear = 4, quadratic = 2, double hashing = 2.
Double hashing matches or beats both earlier methods on every key here.
Notes: All numbers verified by compiling and running each of the three programs on the identical key set. This slide is the direct payoff of reusing the same keys throughout - the improvement is measured, not asserted.

## Slide 8
LECTURE 29
All three methods, side by side
TCS302 - UNIT III
08
Aspect | Linear | Quadratic | Double hashing
Step pattern | always +1 | +1, +4, +9, ... | +step(key) each time
Clustering risk | primary AND secondary | secondary only, reduced | lowest of the three
Can it fail early? | no (with room left) | yes, if tableSize not prime | no (if tableSize prime)
search(9) probes here | 3 | 3 | 2
search(24) probes here | 4 | 2 | 2
Notes: This table condenses everything verified across both Lecture 28 and today into one reference. Use it as a recap quiz: cover the numeric rows and have students predict which method wins before revealing.

## Slide 9
LECTURE 29 - SUMMARY
Change the step, not just the slot
Quadratic probing: idx = (home + i*i) % tableSize - growing gaps reduce secondary clustering, verified: 24 improved from 3 hops to 2.
Quadratic probing's catch: with a non-prime tableSize, only some offsets are ever reachable - insert can FAIL even with empty slots remaining. Verified directly: insert(32) failed with 5 of 8 slots still free.
Double hashing: idx = (home + i*step(key)) % tableSize - the step itself depends on the key, giving the lowest clustering of the three methods tested.
All three need tableSize chosen carefully - prime sizes avoid the failure modes of both quadratic probing and double hashing.
EXIT TICKET tableSize = 7. Insert 5, 12, 19 using quadratic probing (home = key % 7). Show each probe sequence and the final table.
Notes: Exit ticket answer (verified by running the code): all three keys share home index 5 (5%7=5, 12%7=5, 19%7=5). insert(5): i=0, index 5 empty, placed at 5. insert(12): i=0 index5 occupied, i=1 index6 empty, placed at 6. insert(19): i=0 index5 occupied, i=1 index6 occupied, i=2 index(5+4)%7=2 empty, placed at 2. Final table: index 2=19, index 5=5, index 6=12, all others empty.